## Slide 1: Lecture 5: Introduction to Assembly
CS 105

## Slide 2: Programs
#include<stdio.h>
int main(int argc,
char** argv){
printf("Hello
world!\n");
return 0;
}
55
48 89 e5
48 83 ec 20
48 8d 05 25 00 00 00
c7 45 fc 00 00 00 00
89 7d f8
48 89 75 f0
48 89 c7
b0 00
e8 00 00 00 00
31 c9
89 45 ec
89 c8
48 83 c4 20
5d
c3
Notes: A program is a sequence of instructions that specifies how to perform a computation, in a language that a computer can execute
photo: Dorothy Vaughan, computer at Nasa

## Slide 3: Compilation
Pre-
processor
(cpp)
demo05.i
Compiler
(cc1)
demo05.s
Assembler
(as)
demo05.o
Linker
(ld)
demo05
demo05.c
Source
program
(text)
Modified
source
program
(text)
Assembly
program
(text)
Relocatable
object
programs
(binary)
Executable
object
program
(binary)
printf.o
#include<stdio.h>
int main(int argc,
char ** argv){
printf("Hello
world!\n");
return 0;
}
…
int printf(const char *
restrict,
...) __attribute__((__format__ (__printf__, 1, 2)));
…
int main(int argc,
char ** argv){
printf("Hello
world!\n");
return 0;
}
pushq %rbp
movq %rsp, %rbp
subq $32, %rsp
leaq L_.str(%rip), %rax
movl $0, -4(%rbp)
movl %edi, -8(%rbp)
movq %rsi, -16(%rbp)
movq %rax, %rdi
movb $0, %al
callq _printf
xorl %ecx, %ecx
movl %eax, -20(%rbp)
movl %ecx, %eax
addq $32, %rsp
popq %rbp
retq
55
48 89 e5
48 83 ec 20
48 8d 05 25 00 00 00
c7 45 fc 00 00 00 00
89 7d f8
48 89 75 f0
48 89 c7
b0 00
e8 00 00 00 00
31 c9
89 45 ec
89 c8
48 83 c4 20
5d
c3
Notes: M-x hexl-mode to view files in binary

## Slide 4: gcc Option Summary
Output options
  Default is a.out
  -o <filename>, output goes to the named file
  -c, compile but do not link; output goes to program.o
  -S, assemble only; output goes to program.s
  -E, pre-process only; output goes to program.i
Optimization options (uppercase “Oh,” not zero!)
  -O, –O1, –O2, –O3, -Og, -Os
Debugging option: -g, include symbolic debugging information
Warning option example: -Wall
Library option example: -lm, link with the math library

## Slide 5: x86-64 Assembly Language
Evolutionary design, going back to 8086 in 1978
  Basis for original IBM Personal Computer, 16-bits
Intel Pentium 4E (2004): 64 bit instruction set
High-level languages are translated into x86 instructions and then executed on the CPU
  Actual instructions are sequences of bytes
  We give them mnemonic names

## Slide 6: Assembly/Machine Code View
Memory
0x7FFF
0x0000
Central Processing Unit (CPU)
Programmer-Visible State
  PC: Program counter (%rip)
  Register file: 16 Registers
  Float registers
  Condition codes
    Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
PC
Addresses
Instructions
Code
Data
Stack
Heap
Registers
Condition
Codes
Float registers

## Slide 7: Program Counter
Stores the address of the next instruction to execute
Repeat forever:
  Fetch instruction at address in PC
  Execute the instruction
  Update PC

## Slide 8: Assembly Characteristics: Instructions
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic operations on register or memory data
Transfer control
  Conditional branches
  Unconditional jumps to/from procedures

## Slide 9: Data Transfer in Assembly

## Slide 10: Data Movement Instructions
MOV source, dest Moves data source->dest
dest = source

## Slide 11: Operand Forms
Immediate:
  Syntax: $Imm Value: Imm Example: $47
Register:
  Syntax: r Value: R[r] Example: %rbp
Memory (Absolute):
  Syntax: Imm Value: M[Imm] Example: 0x4050
Memory (Indirect):
  Syntax: (r) Value: M[R[r]] Example: (%rsp)
Notes: Note: done on board

## Slide 12: Exercise: Operands
What are the values of the following operands (assuming register and memory state shown above)?
  %rax
  0x104
  $0x108
  (%rax)
Register | Value
%rax | 0x100
%rcx | 0x01
%rdx | 0x03
Memory Address | Value
0x100 | 0xFF
0x104 | 0xAB
0x108 | 0x13
Notes: 0x100
0xAB
0X108
0xFF

## Slide 13: Operand Forms
Immediate:
  Syntax: $Imm Value: Imm Example: $47
Register:
  Syntax: r Value: R[r] Example: %rbp
Memory (Absolute):
  Syntax: Imm Value: M[Imm] Example: 0x4050
Memory (Indirect):
  Syntax: (r) Value: M[R[r]] Example: (%rsp)
Memory (Base+displacement):
  Syntax: Imm(r) Value: M[Imm+R[r]] Example: 12(%rsp)
Memory (Scaled indexed):
  Syntax: Imm(r1, r2, s) Value: M[Imm+R[r1]+R[r2]*s] Example: 7(%rdx, %rdx, 4)
Notes: Note: done on board

## Slide 14: Exercise: Operands
What are the values of the following operands (assuming register and memory state shown above)?
  4(%rax)
  0(%rax,%rcx,4)
  0(%rax,%rdx,4)
  4(%rax,%rcx,4)
Register | Value
%rax | 0x100
%rcx | 0x01
%rdx | 0x03
Memory Address | Value
0x100 | 0xFF
0x104 | 0xAB
0x108 | 0x13
0x10C | 0x47
Notes: 0xAB
0xAB
0X47
0x13

## Slide 15: mov Operand Combinations
Cannot do memory-memory transfer with a single instruction
mov
Mem
Reg
Source
Dest
Imm
Reg
Mem
Reg
Reg
Mem
C Analog
mov $0x4,%rax
temp = 4;
mov $-147,(%rax)
*p = -147;
mov %rax,%rdx
temp2 = temp1;
mov %rax,(%rdx)
*p = temp;
mov (%rax),%rdx
temp = *p;
Src,Dest

## Slide 16: Exercise: Moving Data
For each of the following move instructions, write an equivalent C assignment
  mov $0x40604a, %rbx
  mov %rbx, %rax
  mov $47, (%rax)
Notes: x = 0x40604a y = x *y = 47

## Slide 17: Sizes of C Data Types in x86-64
C declaration | Size (bytes) | Intel data type | Assembly suffix
char | 1 | Byte | b
short | 2 | Word | w
int | 4 | Double word | l
long | 8 | Quad word | q
char * | 8 | Quad word | q
float | 4 | Single precision | s
double | 8 | Double precision | l

## Slide 18: Data Movement Instructions
MOV source, dest Move data source->dest
  movb Move 1 byte
  movw Move 2 bytes
  movl Move 4 bytes
  movq Move 8 bytes

## Slide 19: X86-64 Integer Registers
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
%ax
%al
%bx
%bl
%cx
%cl
%dx
%dl
%si
%sil
%di
%dil
%sp
%bsl
%bp
%bpl

## Slide 20: X86-64 Integer Registers
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
(second argument)
(first argument)
(stack pointer)
(third argument)
(fourth argument)
(function result)
(fifth argument)
(sixth argument)

## Slide 21: Exercise: Translating Assembly
decode:
movq (%rdi), %rax
movq (%rsi), %rcx
movq %rax, (%rsi)
movq %rcx, (%rdi)
ret
void decode(long *xp, long *yp){
}
Register | Use(s)
%rdi | Argument xp
%rsi | Argument yp
Write a C function void decode1(long *xp, long *yp) that will do the same thing as the following assembly code:
Notes: long temp1 = *xp;
long temp2 = *yp;
*yp = temp1;
*xp = temp2;

## Slide 22: C is close to Machine Language
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 23: Arithmetic in Assembly

## Slide 24: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
    xorq Src,Dest Dest = Dest ^ Src
    shlq Src,Dest Dest = Dest << Src Also called salq
    shrq Src,Dest Dest = Dest >> Src Logical
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
char | b | 1
short | w | 2
int | l | 4
long | q | 8
pointer | q | 8
Suffixes
Notes: different signed and unsigned multiply b/c need to set condition bits differently (e.g., overflow for -1*-1 vs 0xFFFF*0xFFFF

## Slide 25: Some Arithmetic Operations
One Operand Instructions
    notq Dest Dest = ~Dest
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
char | b | 1
short | w | 2
int | l | 4
long | q | 8
pointer | q | 8
Suffixes

## Slide 26: Exercise: Assembly Operations
Sum | Location
addq $0x47, %rax
addq %rbx, %rax
addq (%rbx), %rax
addq %rbx, (%rax)
addq 8(%rax,%rdi,8), %rax
Register | Value
%rax | 0x100
%rbx | 0x108
%rdi | 0x01
Address | Value
0x100 | 0x012
0x108 | 0x89a
0x110 | 0x909
Notes: D(rb,ri,S) = D + rb + ri*S
0x147 %rax
0x208 %rax
0x99a %rax
0x11a 0x100
0xa09 %rax

## Slide 27: Example: Translating Assembly
arith:
orq %rsi, %rdi
sarq $3, %rdi
notq %rdi
movq %rdx, %rax
subq %rdi, %rax
ret
Interesting Instructions
  sarq: arithmetic right shift
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | return value
long arith(long x, long y, long z){
x = x | y;
x = x >> 3;
x = ~x;
long ret = z - x;
return ret
}

## Slide 28: Exercise: Translating Assembly
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
arith:
movq %rdi, %rax
addq %rsi, %rax
addq %rdx, %rax
movq %rsi, %rdx
salq $3, %rdx
movq $47, %rcx
addq %rdx, %rcx
imulq %rcx, %rax
ret
long arith(long x, long y,
long z){
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | return value
Notes: long ret = x+y+z;
z = y * 8;
long temp = 47;
temp = temp + z
return temp*ret;

## Slide 29: lea Instruction
Scaled Memory Operands
movq (%rdi,%rsi,8), %rax
leaq Source, Dest
leaq (%rdi,%rsi,8), %rax
pointer arithmetic
  E.g., p = x + i;
arithmetic
  expressions x + k*y (k=1, 2, 4, 8)
void ex(long* xp, long* yp){
long* p = xp + 8*yp;
long ret = *p;
}
void ex(long* xp, long* yp){
long* ret = xp + 8*yp;
}
void ex(long xp, long yp){
long ret = xp + 8*yp;
}
long m12(long x){
return x*12;
}
leaq (%rdi,%rdi,2), %rax # ret <- x+x*2
salq $2, %rax # return ret<<2
Converted to ASM by compiler:

## Slide 30: Address Computation Instruction
leaq Source, Dest
  Source is address mode expression
  Set Dest to address denoted by expression
Example: leaq (%rdi,%rdi,2), %rax
Uses
  Computing pointer arithmetic without a memory reference
    E.g., translation of p = &(x[i]);
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
salq $2, %rax # return t<<2
Converted to ASM by compiler:
p = x+i;
Notes: Note: need to motivate this move on board before start on this