## Slide 1: Lecture 7: Procedure Calls in Assembly
CS 105 Fall 2024

## Slide 2: Review: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
  16 Registers
  Condition codes
    Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
PC
Registers
Addresses
Data
Instructions
Condition
Codes
Code
Data
Stack
Heap
Memory
CPU
0x7FFF
0x0000

## Slide 3: Review: X86-64 Integer Registers
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
(second argument)
(first argument)
(stack pointer)
(third argument)
(fourth argument)
(function result)
(fifth argument)
(sixth argument)

## Slide 4: Review: Assembly Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Conditional branches
  Jumps to/from procedures

## Slide 5: Procedures
Procedures provide an abstraction that implements some functionality with designated arguments and (optional) return value
  e.g., functions, methods, event handlers
To support procedures at the machine level, we need mechanisms for:
  Passing Control: When procedure P calls procedure Q, program counter must be set to address of Q, when Q returns, program counter must be reset to instruction in P following procedure call
  Passing Data: Must handle parameters and return values
  Allocating memory: Q must be able to allocate (and deallocate) space for local variables

## Slide 6: The Stack
the stack is a region of memory (traditionally the "top" of memory)
grows "down"
provides storage for functions (i.e., space for allocating local variables)
%rsp holds address of top element of stack
Stack
0x7FFFFFFF
%rsp
0x00000000
Text
Code
Heap
%rip

## Slide 7: Modifying the Stack
pushq S:
  R[%rsp] R[%rsp] – 8
  M[R[%rsp]] S
popq D:
  D M[R[%rsp]]
  R[%rsp] R[%rsp] + 8
explicitly modify %rsp:
  subq $4, %rsp
  addq $4, %rsp
modify memory above %rsp:
  movl $47, 4(%rsp)
Stack
0x7FFFFFFF
%rsp
S
0x00000000
Text
Code
Heap
%rip
47

## Slide 8: Modifying the Stack
call f:
  pushq %rip
  movq &f, %rip
ret:
  popq %rip
Stack
0x7FFFFFFF
%rsp
0x00000000
Text
Code
Heap
%rip
old %rip
47

## Slide 9: Example: Modifying the Stack
int proc(int* p){
return p[3];
}
int example1(int x) {
int a[4];
a[0] = 13;
a[1] = 47;
a[2] = 105;
a[3] = 41;
return proc(a) + 1;
}
example1:
subq $16, %rsp
movl $13, (%rsp)
movl $47, 4(%rsp)
movl $105, 8(%rsp)
movl $41, 12(%rsp)
movq %rsp, %rdi
call 0x400596 <proc>
addl $1, %rax
addq $16, %rsp
ret
proc:
movl 12(%rdi), %eax
ret
Notes: Walk through on board, then demo
Demo 1 - Procedure calls (note: run on linux server):
make example1
gdb example1
(gdb) b example1 # set breakpoint at beginning of function example1
(gdb) disassem example1 # show assembly code and walk through
(gdb) r
(gdb) info reg # observe values in %rsp and %rip
(gdb) stepi
(gdb) info reg # observe new values of %rsp and %rip
(gdb) x/4wd $rsp # see initial values in a as ints
(gdb) step i
(gdb) x/4wd $rsp # observe new array values (a[3] now 10)
(gdb) x/3gx $rsp # observe return address value
(gdb) disassem main # observe ret addr is next instr in main

## Slide 10: Exercise 1: Modifying the Stack
0x400557 <fun>:
400557: movq $13, 16(%rsp)
40055a: ret
0x40055b <main>:
40055b: sub $8, %rsp
40055f: pushq $47
400560: callq 400557 <fun>
400565: popq %rax
400566: addq (%rsp), %rax
40056a: addq $8, %rsp
40056e: ret
%rsp
47
0x400565
13
%rip
%rax
47
60
What's the value in %rax immediately before the instruction at 0x40056e is executed?
What's the value in %rsp immediately before the instruction at 0x40056e is executed?
0x40056f
0xf0
0xe8
0xe0
0xd8
0xd0
0xc8
0xc0
0xb8

## Slide 11: Procedure Calls (simplified)
Caller
Before
  Put arguments in place (if there are parameter vars)
  Make call
After
  Use result (if non-void)
Callee
Preamble
  Allocate space on stack (if needed)
Exit code
  Put return value in place (if non-void function)
  Deallocate space on stack (if allocated)
  Return

## Slide 12: Example: Modifying the Stack
int example1(int x) {
int a[4];
a[0] = 13;
a[1] = 47;
a[2] = 105;
a[3] = 41;
return proc(a) + 1;
}
example1:
subq $16, %rsp
movl $13, (%rsp)
movl $47, 4(%rsp)
movl $105, 8(%rsp)
movl $41, 12(%rsp)
movq %rsp, %rdi
call 0x400596 <proc>
addl $1, %rax
addq $16, %rsp
ret
allocate
args
dealloc.
return
ret. val
call

## Slide 13: Maintaining Variable state
function:
movl $47, %rbx
movl $13, %rdi
call 0x40042a <mystery>
# what is in %rbx?
# what is in %rdi?
ret
int function(){
int x = 47;
int y = 13;
mystery(y);
// what is x?
// what is y?
}
Notes: walk through two options: caller-saved, callee-saved

## Slide 14: X86-64 Register Usage Conventions
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
(second argument)
(first argument)
(stack pointer)
(third argument)
(fourth argument)
(function result)
(fifth argument)
(sixth argument)
Callee-saved registers are shaded

## Slide 15: Procedure Calls, Division of Labor
Caller
Before
  Save caller-saved registers to stack (if used after call)
  Put arguments in place (if there are parameters)
  Make call
After
  Restore caller-saved register (if used after call)
  Use result (if non-void)
Callee
Preamble
  Save callee-saved registers (if will use)
  Allocate space on stack (if needed)
Exit code
  Put return value in place (if non-void function)
  Restore callee-saved registers (if used)
  Deallocate space on stack (if allocated)
  Return

## Slide 16: Exercise 2: Value Passing
0x400540 <last>:
400540: mov %rdi, %rax
400543: imul %rsi, %rax
400547: ret
0x400548 <first>:
400548: lea 0x1(%rdi),%rsi
40054c: sub $0x1, %rdi
400550: callq 400540 <last>
400555: rep; ret
0x400556 <main>:
400560: mov $4, %rdi
400563: callq 400548 <first>
400568: addq $0x13, %rax
40056c: ret
What value gets returned by main?
%rsp
%rdi
%rsi
%rax
0x400560
%rip
4
0x400568
0x400563
0x400548
5
0x40054c
0x400550
3
0x400540
0x400555
0x400543
3
0x400547
15
0x400555
0x400568
0x40056c
34
0x400560

## Slide 17: Handling Extra Parameters
Conventions define 6 registers for storing arguments
If function has more than 6 parameters, additional arguments go on the stack

## Slide 18: Procedure Call Example: Arguments
int func1(int x1, int x2, int x3,
int x4, int x5, int x6,
int x7, int x8){
int l1 = x1+x2;
int l2 = x3+x4;
int l3 = x5+x6;
int l4 = x7+x8;
int l5 = 4;
int l6 = 13;
int l7 = 47;
int l8 = l1 + l2 + l3 + l4 + l5
+ l6 + l7;
return l8;
}
int main(int argc, char *argv[]){
int x = func1(1,2,3,4,5,6,7,8);
return x;
}
func1:
addl %edi, %esi
addl %ecx, %edx
addl %r9d, %r8d
movl 16(%rsp), %eax
addl 8(%rsp), %eax
addl %esi, %edx
addl %r8d, %edx
leal 64(%rax,%rdx), %eax
ret
main:
movl $1, %edi
movl $2, %esi
movl $3, %edx
movl $4, %ecx
movl $5, %r8d
movl $6, %r9d
pushq $8
pushq $7
callq _function1
addq $16, %rsp
retq
Notes: note: clang actually assembly adds pushq rax to beginning and popq rcx to end to align to 16 bytes (seen in demo)

## Slide 19: Stack Frames
Each function called gets a stack frame
Passing data:
  calling procedure P uses registers (and stack) to provide parameters to Q.
  Q uses register %rax for return value
Passing control:
  call <proc>
    Pushes return address (current %rip) onto stack
    Sets %rip to first instruction of proc
  ret
    Pops return address from stack and places it in %rip
Local storage:
  allocate space on the stack by decrementing stack pointer, deallocate by incrementing
return address
0x7FFFFFFF
0x00000000
Stack
…
local variables
saved registers
local variables
Arguments 7..n
%rsp
Text
Code
Heap
%rip

## Slide 20: Recursion
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the C code explicitly does so (more later!)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 21: Array Recursion
sum_digits_r:
cmp $4, %rsi
jle L2
mov $0, %rax
ret
L2:
push %rbx
mov (%rdi,%rsi,4), %ebx
incr $1, %rsi
call sum_digits_r
add %ebx, %eax
pop %rbx
ret
int sum_digits_r(int* z, int i){
if(i >= 5){
return 0;
}
int val = z[i];
int sum_r = sum_digits_r(z,i+1);
return sum + val;
}
Notes: Discussion: compare the differences, then On board: work through stack for this example. then Demo: recursive function
(gdb) disassem sum_digits_r # show assembly
(gdb) b *0x400563 # set breakpoint at base case ret
(gdb) r
(gdb) bt # show stack trace
(gdb) x/10gx # show contents of stack and compare to diagram on board
(gdb) disassem sum_digits_r # find stored return address in assembly code
(gdb) c # continue to end (main prints return value)

## Slide 22: Example: Array Recursion
%rsp
36
%rdi
0
%rsi
47
%rax
47
1
&add
0
9
1
7
1
1
36
40
44
48
52
56
%rbx
47
9
9
1
2
&add
1
7
3
&add
7
1
4
&add
1
5
&add
1
2
7
9
1
10
9
19
47
sum_digits_r:
cmp $4, %rsi
jle L2
mov $0, %rax
ret
L2:
push %rbx
mov (%rdi,%rsi,4), %ebx
incr $1, %rsi
call sum_digits_r
add %ebx, %eax
pop %rbx
ret
Notes: Discussion: compare the differences, then On board: work through stack for this example. then Demo: recursive function
(gdb) disassem sum_digits_r # show assembly
(gdb) b *0x400563 # set breakpoint at base case ret
(gdb) r
(gdb) bt # show stack trace
(gdb) x/10gx # show contents of stack and compare to diagram on board
(gdb) disassem sum_digits_r # find stored return address in assembly code
(gdb) c # continue to end (main prints return value)